## Slide 1: Configuration Management Game
Introduction
by Martijn Dullaart
mdux.net/cm-game
Based on the CM Effectivity Game from ASML Original creator: Arnaud Hubaux Co-creators: Pauline Francken, Willem-Jan Span & Martijn Dullaart
Rev 3

## Slide 2
Disclaimer
The views and opinions expressed in this and related documents are those of the author and do not necessarily reflect any views or opinions of his employer or any of its employees. The information is provided AS-IS and without any warranties. This information could contain inaccuracies, typographical errors and out-of-date information. This document may be updated or changed without notice at any time. Use of the information is therefore at your own risk. In no event shall the author be liable for special, indirect, incidental or consequential damages resulting from or related to the use of this and related documents.
Rev 3
Credits
CM Game (mdux.net/cm-game) by Martijn Dullaart, is licensed under CC BY-SA 4.0, and is based on the original CM effectivity Game from ASML. Original Creator: Arnaud Hubaux; Co-creators: Pauline Vrancken, Willem-Jan Span and Martijn Dullaart.

## Slide 3
Can you Design, Order, Supply and Build the right configuration?
From Left to Right: Modiefied “LEGO GUY” © SRBrandon, license CC BY-SA 2.0; Modified “LEGO Administrative Professionals” © Willis Lam, license CC BY-SA 2.0; Modified “LEGO Business Woman” © Willis Lam, license CC BY-SA 2.0; Modified "Project 365 #14: 140117 Happy Days!" © Pete, license CC BY 2.0
Disclaimer: The Minifigure and the Brick and Knob configurations are trademarks of the LEGO group. LEGO® Is a trademark of the LEGO Group of companies which does not sponsor, authorize or endorse this game.
Orders
I want this truck
Rev 3

## Slide 4
Game Plan
We need: Engineers, Suppliers and Operations people to deliver the Truck
Setup:
Each team consists of 3 sub teams: Engineering, Operations and Suppliers
Roles:
Game:
You will get detailed game instructions and have to create product documentation, purchase and production orders, build Assemblies and a Final Assembly of a Truck within the 25 minutes. Every minute is representing a week in the schedule, you will see the clock on the screen.
Winner: The first team that passes the customer verification
Customer
Engineering
Operations -
Supply Chain Mgt
Supplier
Operations -
Factory
Rev 3
Notes: Note that Operations is mentioned twice. Once as supply chain mgt for ordering parts at the supplier and once as factory to build the Hybrid Pickup Truck

## Slide 5
Learning Objectives
Understand and apply 3 key principles of Configuration Management
Effective dates determine when documents and parts can be used
Documents lead, parts follow
Planning is the only way to control part usage in operations
Rev 3

## Slide 6
time
Specification
3D model
Bill of Material
Instruction
Development
Supply
Factory
Build & Deliver part
Build & Deliver part
Change
Part
Use 123 TPD
Assemble unit 1
Assemble unit 2
Use 456
Use 123
SCM
Use 123 TPD
SCM
Use 456 TPD
Unit 1
Unit 2
Purchase Order
Production order
Use 456 TPD
All you need to know about the 3 key principles
rev = revision
CC-BY-SA 4.0 Rev 3
Configuration Management Game mdux.net/cm-game
TPD = Technical Product Documentation
rev 1
E
R
E
Released
R
Effective
rev 2
E
R
rev 1
R
E
rev 1
R
E
rev 2
R
E
rev 2
R
E
rev 1
R
E
rev 2
R
E
TPD - 123
R
E
TPD - 456
R
E
Notes: Documentation about your product is created over time. So if you want develop a hybrid pickup truck with snow plow, different types of documents will be created like a Specification, 3D Model, Bill of Material, Instructions on how to assemble and the Technical product documentation for parts used in the assembly of the product. E.g. part 123.
The BoM of the product is released early for resource planning (in ERP) but effective (1) at start of production of the product. While Part 123 already needs to be ordered earlier because of lead time. That is why the TPD is effective before the BOM of the assembly/product is effective.
So when TPD is effective, the purchase order can use the TPD of 123 and order the part at the supplier (2). Who can then start manufacturing the part and delivering the part right on time. For the production order of the first Unit of the product that will use part 123.
However life is full of change and part 123 is reaching end of life and needs to be replaced. Several documents of the product require an update (new revision) and TPD for a new part (456) is created. While production order of unit 1 starts, the purchase order for part 456 needs to be created in order for the supplier to deliver the new part (456) in time to start the production of Unit 2, which will use part 456 in stead of 123. That means planning is very important. (3)
Effective = when a document revision is valid for use (should be used for execution like assembly or ordering parts)
Released = when a document revision has been validated (can be used for planning resources, cannot be used in execution like assembly or ordering parts)
Effective dates determine when documents and parts can be used
Documents lead, parts follow
Planning is the only way to control part usage in operations

## Slide 7
Suppliers
Operations
Engineering
Customer
Instructions
ASSY WI
Develop
Pickup Truck
ASSY BOM
FASY BOM
FASY WI
ASSY
Purchase Order
Build ASSY
Distribute Supplier TPD
ASSY BOM+WI
Customer requirements
Week 0
Customer signoff
Week 17
Production Order
Distribute Factory TPD
Build FASY
FASY BOM+WI
Document
Action
Physical
Customer
Operations
Engineering
Supplier
FASY
Abbreviations:
ASSY = Assembly
FASY = Final Assembly
WI = Work Instructions
BOM = Bill of Material
TPD = Technical Product Documentation (BOM + WI)
PO = Purchase Order
Rev 3
Notes: Make sure people do not pickup the documentation from the table or start investigating the materials.
As facilitator, I’m the customer. And I have given you the requirements, which are on the Engineering team tables.
Engineering will develop the pickup truck by creating the Assy (assembly) Bill of material (BOM) and Work instructions (WI). Yes we tell our suppliers how to build the assembly ;-). The ASSY BOM and WI will be given to the operations team.
Same for the Final Assembly (FASY) BOM and work instructions (WI).
The operations team has 2 functions: Supply Chain mgt and Manufacturing (factory). Operations will distribute the Supplier Technical Product Documentation (TPD aka BOM and WI in this game) with a Purchase order to the supplier. And the supplier will upon receipt of the Purchase order and TPD start work based on effective date of the documentation.
The operations team will also distribute the factory TPD (BOM and WI) with a production order to the factory (within operations). And upon receipt will start working based on the effective date of the documentation.
When in Week 17 the work is done you can come to the customer, me, for customer validation and signoff.

## Slide 8
Team Setup
Split each team in Engineering (3 - 4), Supplier (1 or 2) and Operations (2 - 4)
Room
Team 9 Engineering
Team 10
Engineering
Team 9
Operations
Team 10
Operations
Team 9
Supplier
Team 10
Supplier
Rev 3
Notes: Preferred team size is 7 to 10 people.
3 tables per team: one for Engineering, one for Operations and one for Supplier.
Color coding and numbering can help keep the teams apart.
Optionally put the suppliers outside of the room.
Dividers in the room can help with creating the divide between departments.

## Slide 9: Start
Let’s Play
Rev 1
Notes: For a clock on the screen you can use google stopwatch.

## Slide 10: Wrap up
How was it?
Rev 1

## Slide 11
Wrap Up
Key take away
Did you use the effectivity mechanism?
Would the same effectivity mechanism apply to software?
Do you miss anything to build an exact copy of the first unit right now?
How well did your team control the plan? How could you have improved this?
Rev 3
Notes: In most cases people completely ignore the effectivity mechanism, because of the stress. Only once or twice out of the 40+ teams that did the game, the effectivity mechanism was properly used.
Yes it would, how else would you ensure that the right version of the software is available for a specific configuration.
To be efficient yes, only the delta documentation to change the in work product was created. To make an exact copy efficiently (without waste) you need to update the documentation to build it right from the start.
Some teams assign a specific person within Engineering and a specific person in the operations subteam to make sure everyone is following the plan. These teams tend to perform a lot better.